## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID –SIH26240
Problem Statement Title-Smart Water Purification and Quality Monitoring System for Rural and Mining-Affected Areas
Theme-Smart Automation
PS Category- Hardware
Team ID-SIH26-A0H-T278
Team Name - Nexus

## Slide 2: IDEA TITLE
Nexus
A semi-portable, electric-powered 6-stage purifier designed for difficult water sources near mining and agricultural areas.
CORE CONCEPT
Medium-sized wheeled unit • on-site treatment • battery backup • emergency solar charging
SIX-STAGE TREATMENT
1 pH correction → 2 sediment/rock & grit removal → 3 pre-filtration → 4 RO → 5 carbon polishing → 6 UV/disinfection
DESIGN GOAL
Reduce dissolved salts, metals/chemicals, turbidity and microbes while producing usable treated water
HOW IT ADDRESSES THE PROBLEM
• Built for variable raw-water quality • Replaceable filter modules • Automatic pH/TDS/turbidity monitoring • Reject-water outlet for controlled disposal/reuse
INNOVATION & UNIQUENESS
• Hybrid grid + battery + solar emergency operation • Modular six-stage architecture • Semi-portable chassis for farms, mine-adjacent settlements and field deployment • Sensor-driven protection of RO membrane

## Slide 3: TECHNICAL APPROACH
Nexus
Hardware architecture and treatment flow
1. pH REGULATOR
Dosing pump + pH sensor Balances acidic/alkaline feed
2. GRIT / ROCK REMOVER
Coarse screen + settling chamber Captures stones, sand & heavy solids
3. PRE-FILTER
Sediment + activated-media prefilter Protects RO membrane
4. RO PURIFIER
High-pressure pump + RO membrane Removes dissolved salts and many contaminants
5. CARBON POLISHING
Activated carbon stage Improves taste/odour and reduces residual organics
6. UV / FINAL DISINFECTION
UV-C chamber + final micron filter Controls microbial contamination
POWER SYSTEM
230 V AC primary → charge controller → LiFePO₄ battery → DC/AC loads; solar panel provides emergency/backup charging
CONTROL & SAFETY
ESP32/PLC controller • pH/TDS/turbidity sensors • low-water cutoff • pressure switch • leak protection

## Slide 4: FEASIBILITY AND VIABILITY
Nexus
Feasibility, field operation and risk controls
FEASIBILITY
Commercial RO membranes, pumps, UV modules, sensors and LiFePO₄ batteries are readily available. A wheeled enclosure keeps the system semi-portable.
FIELD OPERATION
Feed tank → 6-stage treatment → clean-water tank. Typical deployment can be designed around 100–250 L/h, subject to feed-water testing and membrane selection.
MAINTENANCE
Scheduled sediment-filter replacement, membrane flushing, UV inspection and calibration of pH/TDS/turbidity sensors.
KEY CHALLENGES
• Highly variable mining/agricultural feed water • RO concentrate management • Membrane fouling/scaling • Power interruptions • Transport weight and water storage
MITIGATION
• Pre-screen + staged filtration • pH control and pressure monitoring • Automatic high-TDS/low-flow alarms • Battery ride-through + solar emergency charging • Lockable wheeled frame and modular service access

## Slide 5: IMPACT AND BENEFITS
Nexus
Expected impact and measurable benefits
TARGET USERS
Mine-adjacent communities • agricultural workers • small farms • field camps • emergency water points
HEALTH & SOCIAL
Provides a controlled treatment train for contaminated/variable raw water; supports safer access to treated water where centralized treatment is limited.
ECONOMIC
Semi-portable deployment reduces dependence on transporting treated water; modular components can be serviced individually.
ENVIRONMENTAL
• Solar emergency charging reduces dependence on grid power • Efficient pre-treatment extends membrane life • Reject water can be separately managed based on contaminant testing
MEASUREMENT PLAN
Track inlet/outlet pH, TDS, turbidity, conductivity and microbial indicators. Compare before/after values and record filter life, energy use and water recovery.

## Slide 6: RESEARCH AND REFERENCES
Nexus
Actual water-quality evidence supporting the design
MINING — IB VALLEY COALFIELD, INDIA
A 2024 study of 102 mine-water/groundwater samples reported mine-water pH of 3.26–8.18. Mn was dominant among several metals; Fe, Mn and Al were major objectionable metals for drinking-water quality.
MINING — IRON-MINING IMPACTED AREA, JHARKHAND
Fe and Mn exceeded drinking-water standards in about 75% of groundwater samples across seasons. Highest metal concentrations occurred near active mining locations.
AGRICULTURE — DHARAPURAM, SOUTH INDIA
A recent groundwater study found TDS above the permissible limit in 11.76% of samples, nitrate in 32.35%, and fluoride in 23.53%. Agricultural runoff was identified as a contributing factor.
AGRICULTURE — THANJAVUR, TAMIL NADU
A groundwater study of 102 samples found 13% with elevated nitrate (>45 mg/L as NO₃). The study linked nitrate/chloride/sulfate patterns to surface contamination including agricultural and domestic activities.
WHAT THIS MEANS FOR OUR HARDWARE
The unit cannot assume one fixed 'dirty-water' profile. Sensor monitoring + staged solids removal + pH control + RO + carbon + UV gives a configurable treatment train for variable field water.
VALIDATION BEFORE DEPLOYMENT
For each selected site, test inlet/outlet pH, EC/TDS, turbidity, nitrate, hardness, Fe/Mn and microbial indicators; add fluoride/arsenic/pesticide tests where local risk warrants. Final removal claims will be based on pilot-test results.
Sources: Pandey et al., Heavy metal geochemistry… Ib Valley coalfield (2024); iron-mining impacted groundwater study, Jharkhand (2023); Dharapuram groundwater nitrate/fluoride study (2025); Thanjavur groundwater study. Standards: BIS IS 10500 / WHO drinking-water guidance.